## Slide 1: System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Wajid Minhass, Paul Pop, Jan Madsen
Technical University of Denmark

## Slide 2: Flow-Based Microfluidic Biochips
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
10 mm
Inlets
Chamber
Outlets
Switches
Waste channels
Manipulations of continuous liquid through fabricated micro-channels

## Slide 3: Outline
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
  Biochip Architecture
  Challenges and Motivation
  System Model
      Component Model
      Biochip Architecture Model
      Biochemical Application Model
  Biochip Synthesis Tasks
  Problem Formulation
  Proposed Solution
      List Scheduling + Contention Aware Edge Scheduling
  Experimental Evaluation
  Conclusions

## Slide 4: Biochip Architecture
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Microfluidic Valve – Multi-Layer Soft Lithography

## Slide 5: Biochip Architecture
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Microfluidic Large Scale Integration (LSI) :
Microfluidic Switch
Valves combined to form more complex units

## Slide 6: Biochip Architecture
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Microfluidic Mixer

## Slide 7: Biochip Architecture
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Microfluidic Mixer

## Slide 8: Biochip Architecture
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Microfluidic Mixer
http://groups.csail.mit.edu/cag/biostream

## Slide 9: Components
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
  Mixer
  Detector
  Filter
  Heater
  Separator
  Storage Units
  …
http://groups.csail.mit.edu/cag/biostream

## Slide 10: Biochip Architecture
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Schematic View
Functional View

## Slide 11: Challenges
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
  Manufacturing technology, soft lithography, advancing faster than Moore’s law
  Increasing design complexity
  Current methodologies
    Full-custom
    Bottom-up
  Radically different, top-down, synthesis and design methodologies required

## Slide 12: System Model
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
  The model considers discretized fluid volumes
  Fluid sample volumes can be precisely controlled (unit sized samples)
  Each sample occupies a certain length on the flow channel using metering

## Slide 13: Metering – Unit Sized Samples
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Metering is done by transporting the sample between two valves that are a fixed length apart
Input
Waste
To other components
Input
Waste
To other components
Input
Waste
To other components
Input
Waste
To other components
open
closed
(a)
(c)
(b)
(d)
Notes: Microfluidic metering process. Open and closed symbols refer to open and actuated control valves, respectively. (a) Sample of interest flows
from an input port through one half of the rotary mixer. (b) Sample is compacted against a valve on the right side of the mixer, ensuring a
consistent cross-sectional area. (c) Excess sample is flushed to the waste port. (d) A unit-sized sample results and can be mixed or transported to
storage

## Slide 14: Component Model
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Microfluidic Mixer
(1) Ip1
Five phases:
Ip1
Ip2
Mix (0.5 s)
Op1
Op2
Flow Layer Model:
Operational Phases + Execution Time

## Slide 15: Component Model
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
closed
(4) Op1
(5) Op2
open
Waste
Input
Waste
Input
Waste
Input
Waste
Input
(2) Ip2
(3) Mix

## Slide 16: Biochip Architecture Model
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips

## Slide 17: Biochip Architecture Model
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Topology graph based model
A = (N, S, D, F, c) , where,
N = All nodes (Switches and Components)
S = Switch nodes only, e.g., S1
D = Directed edge between 2 nodes, DIn1, S1
F = Flow path, i.e., set of two or more directed edges
c = Transport latency associated with a flow path or a directed edge

## Slide 18: Flow paths in the architecture
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Fluid Transport latencies are comparable to operation execution times
Handling fluid transport (communication) is important
Enumerate flow paths in the architecture
F1

## Slide 19: Flow paths in the architecture
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
A flow path is reserved until completion of the operation, resulting in routing constraints
F1
F3

## Slide 20: Biochemical Application Model
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Directed, acyclic, polar
Each vertex Oi represents an operation
Each vertex has an associated weight denoting the execution time

## Slide 21: Biochip Synthesis Tasks
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Allocation
Placement
Binding
Scheduling
  Operation Scheduling
  Edge Scheduling: Routing latencies comparable to operation execution times

## Slide 22: Problem Formulation
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Given
  A biochemical application G
  A biochip modeled as a topology graph A
  Characterized component model library L
Produce
  An implementation minimizing the application completion time while satisfying the dependency, resource and routing constraints
  Deciding on:
    Binding of operations and edges
    Scheduling of operations and edges

## Slide 23: Proposed Solution
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Allocation and Placement: Given
Binding and Scheduling (Operations):
  Greedy Binding + List Scheduling
Fluid Routing (Contention Aware Edge Scheduling)
  Greedy Binding + List Scheduling

## Slide 24
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
F15
F14

## Slide 25
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
No flow path from Heater1 to Mixer 3!
F30-1
F26-1
A composite route

## Slide 26: Design Methodology
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Biochemical Application Model
Binding and Scheduling
Routing
Optimization
Control Layer Model
Flow Layer Model
Control Layer Model
Graph-based Model
Flow Path
Generation
Control
Synthesis
Biochip Controller
Design Implementation
Component Library
Synthesis
Biochip
Architecture Model

## Slide 27: Experimental Results
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Synthesizing two Real Life Assays and one Synthetic Benchmark

## Slide 28: Experimental Results
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Varying number of I/O Ports

## Slide 29: Conclusions
12/10/2011
System-Level Modeling and Synthesis of Flow-Based Microfluidic Biochips
Proposed
  a component model for the fluidic components
  an architecture model for the flow-based microfluidic biochips
Proposed a system-level modeling and simulation framework for flow-based biochips
  reduced design cycle time
  facilitating programmability and automation
Demonstrated the approach by synthesizing two real life assays and four synthetic benchmark on different biochip architectures